Name	Description	Formula	Symbols in the formula
gl_melt_cumul	This is the cumulative melt (of snow, firn, and ice) averaged over the entire glacier surface. / It starts from 0.0 on the first day of the simulation, and is updated every day. / The unit is either (1) meter water equivalent, or (2) millimeter water equivalent: this is decided in set_params.R (variable output_unit, under “PLOTTING parameters”)	gl"_"melt"_"cumul_i ~=~ {sum from{j=1} to{i} { sum from{k=1} to {N} {M(j, k)}}} over { N }	i is the number of the day up to which the cumulative value is calculated. / j is the number of each day in the model, from 1 (the start) until i (so for example if i = 6, j will be 1, 2, 3, 4, 5, 6). / k is the number of each grid cell of the model, considering only grid cells inside the glacier. / N is the total number of grid cells in the model which are inside the glacier. / M(j, k) is the melt calculated by the model at day j for grid cell k. Melt is calculated depending on surface type, following the equations in file melt_surface_equations.pdf.
gl_melt_cumul_bandcorr	This is the same as the previous one (gl_melt_cumul), but with an additional correction based on the contour-line method. / The model calculates the error of the simulated mass balance compared to the stake measurements, within each altitude band (for example, the error at 3500-3600 m, the error at 3600-3700 m, and so on). Then from this error the model calculates a correction factor which is applied to the grid cells of that elevation band. / This correction factor is local (one different correction for each elevation band), but it can also change the total mass balance (usually small change, because the model is calibrated against the stakes).	gl"_"melt"_"cumul"_"bandcorr~=~newline "="~ gl"_"melt"_"cumul `cdot` f_corr newline newline f_corr~=~MB_cc / MB_orig	gl_melt_cumul is the previous one. / fcorr is the correction factor. / MBcc is the glacier mass balance calculated by the model and corrected with the elevation bands (see description). / MBorig is the original glacier mass balance, as calculated by the model.
gl_melt_daily_m3	This is the daily melt (of snow, firn and ice located on the glacier) expressed in cubic meters. / It is shown in red (“Melt”) in the plot of “Water fluxes” (page 8 of PDF file e.g. massbalance_2021.pdf, under annual_results)	gl"_"melt"_"daily"_"m3~=~gl"_"melt"_"daily `cdot`A_gl	gl_melt_daily is the average glacier-wide melt simulated on a certain day, expressed in meters water equivalent. / Agl is the total surface area of the glacier, in square meters.
gl_melt_daily_m3_bandcorr	This is the same as the previous one (gl_melt_daily_m3), but it is calculated after the contour-line correction (see description of gl_melt_cumul_bandcorr).	gl"_"melt"_"daily"_"m3"_"bandcorr~=~newline "="~gl"_"melt"_"daily"_"m3 `cdot` f_corr	gl_melt_daily_m3 is the previous one. / fcorr is the correction factor (the same as for gl_melt_cumul_bandcorr).
gl_rainfall_daily_m3	This is the amount of rain which falls on the glacier in one day. / It is calculated from the total precipitation, the temperature (to select liquid/solid precipitation) and the surface area of the glacier. / It is shown in light blue (“Rainfall”) in the plot of “Water fluxes” (page 8 of PDF file e.g. massbalance_2021.pdf, under annual_results)	gl"_"rainfall"_"daily"_"m3~=~newline "=" ~{sum from {k=1} to {N} {P ( k ) cdot (1-f_s(k))}} over { N }`cdot`A_gl	P(k) is the total precipitation (solid + liquid) which falls on cell k on a certain day, expressed in meters water equivalent. / fs is the fraction of solid precipitation at cell k; it depends on temperature. / See the formulas in file DMBSim_model_description.pdf for the calculation of P and fs from the station data (that file uses cell coordinates x and y instead of cell number k, but the calculation is the same). / N is the total number of grid cells in the model which are inside the glacier. / Agl is the total surface area of the glacier, in square meters.
gl_scaf	This is the fraction of the glacier surface which is covered by snow at the beginning of each day. / It is expressed in percent (%).	gl"_"scaf~=~100`cdot`{N_snow `cdot`A_cs`} over A_gl	Nsnow is the number of cells which have surface type “snow” at the start of the day. / Acs is the surface area of each grid cell. / Agl is the total surface area of the glacier.

Glacier runoff from the model can be calculated as the sum of gl_melt_daily_m3 and gl_rainfall_daily_m3. The result is expressed in m3/day. Note that the model does not consider water refreezing in the body of the glacier.